DSC03系列步进定位控制系统

系统采用基于先进的ARM内核的32位单片机，主传动采用变频调速，薄膜牵引采用二轴或三轴步进驱动。温度控制采用自整定PID控制方式，控制精度达到±1℃。本系统具有制袋速度快，牵引定位准，温度控制稳定等优点。系统具有倍送，计数，冲孔，故障检测，自动报警停车等功能，适用于中封，三边封，站立袋，拉链袋等多种机型。

系统性价比高，低成本高性能，是简易制袋机的理想选择！

主要技术指标：

- 制袋长度：30~450毫米，超长采用倍送

- 制袋速度：最高段速为180段/分钟

- 线速度：  最高线速为40米/分钟；

- 定位精度：±0.2毫米

- 步距角范围：400-1200步/转

- 倍送功能：最大6倍送

- 冲孔功能：有禁止，连续，间隔三种方式可选

- 温度控制：最多可达24路，控制稳定度优于±1℃

DSC03 Series step motor positioning control system

The system is based on ARM. Step Motor drives film feed. A Inverter drives the main motor to move heaters up and down, another Inverter drives the unwinding motor to unwind the film. Temperature control, based on self-PID control, is better than ± 1 ℃. The system has times delivering, counting, punching, detecting fault , automatic alarm parking and other functions. Applicable to middle-sealing bag machine, three-edges-sealing bag machine, self-support bag machine, slide fastener bag machine, and so on.

The cost-performance ratio of the systerm is low, low cost and high performance. It’s your optimal choice for the simple bag-making machine.

Main technical parameters:

- Bag-making Length: 30-500mm, longer use times mode

- Bag-making Speed: The maximum speed is 180 Pcs / min;

- The velocity of unwinding film：The maximum velocity is 40m/min.

- Length Tolerance: ±0.2mm.

- step angle range:  0.9°- 0.3°

- Times mode:  up to 6 times.

- Punch mode:  Opt among prohibited, continuous, alternation.

- Temperature control:

- Temperature units: up to 20 units.

- Temperature interval: up to 500℃.

- Temperature tolerance: ± 1 ℃.

- Total power requirements: 20kw / 380VAC+10％, 50Hz.